#### Sample Questions, CSc 137 Midterm Exam, Spring 2018
I. True/False
1. _T_   A decoder decodes a binary input to a unary output.
2. _T_   A multiplexor chooses one of multiple input as its single output.
3. _F_   To program a Verilog code module that performs the boolean function AB+CD, a minimum of 5 logic-gate statements are needed.
   3 needed
4. _F_   If a multiplexor is given k select input signals, it can only select one output from this many input: 2 times k.
   2 to the power of k
5. _F_   When input to a decoder is 1012, then the output would be 00001000.
   00000100
II. Multiple Choice
1. _C_   Which below is not in a Full Adder:
  1. a sum bit
  2. a carry-in bit
  3. a overflow bit
     overflow is the last carry-out in a multi-adder
  4. a carry-out bit
  5. two bits in input to sum
2. _C_   How many components are there in the BC CPU that write to the common bus?
  1. 5
  2. 6
  3. 7
  4. 8
  5. 9
3. _D_   An "Indirect" memory-reference instruction has extra work at the clock cycle T (number?)
  1. 0
  2. 1
  3. 2
  4. 3
  5. 4
III. Fill-out Blanks
1. The CPU is controlled by this component (two words): __Control__Unit__
2. from which its function is to generate (two words) __Control__Signals__.
3. The timing device in the control unit is called (two words) __Sequence__Counter__
4. which it is a counter of (how many) __4__ binary bits,
5. and this can indicate a total of (how many) __16__ T-steps. 2^4
6. D0 through D7 are decoded results from this CPU register: __IR__.
IV. Concise Answers
1. Given the Bus Diagram (Figure 5-4, p. 130) and the Control functions and Microoperations (Table 5-6, p. 159), derive the control signals needed to each of the CPU instructions. (Similar to exercise questions.)
  selected instA: do-X, do-Y, ...
  selected instB: do-X, do-Z, ...
  selected instC: do-W, do-Y, ...
  ...
2. Derive timing for each of control signal derived from above. (Similar to exercise questions.)
3. Given code of a Verilog module, draw out the circuit diagram.
4. Given this gate-logic diagram, write Verilog code for this module. (No Test module needed. Arrays usage may be required.)
module Xmod(A, B, C); / input A, B; / output C; / wire invB; / not(invB, B); / and(C, A, invB); / endmodule / module Ymod(A, B, C, F); / input A, B, C; / output F; / wire invA, invB, X1out, X2out, andAB; / not(invA, A); / not(invB, B); / Xmod X1(C, invA, X1out); / Xmod X2(invB, A, X2out); / and(andAB, A, B); / or(F, X1out, X2out, andAB); / endmodule