COMMON BUS SYSTEM

hidden in the background the adder logic
and the output will be latched to the AC accumulator

input is using clock, output is continuous

though registers and memory need clock, adders and other programs do not need the clock
memory for what? Memory will change in the future, output stays
eternal memory is counted as one type of input

if you have memory building, like sequential circuit, it will hold part of the output for the next input

combinational circuit, like decoders and multiplexors
sequential circuit are feedback

BC instruction cycle
T0 is from the sequence counter where the binary is decoded to unary
counter is not binary by default?
4-bit binary system, 4-bit sequential counter
increment or clear to 0

Control Unit of a basic computer
close-up of instructon register
single wire on T0 is true,

instructions also go thru decoding
3x8 decoder

INSTRUCTION CYCLE
T0 from the previous slide
T1 from IR, Memory addressed by AR will fetch 16-bit output
propagate to the bus and the other components will receive
decoded result T2 D0..D7 will be

DETERMINE THE TYPE OF INSTRUCTION flowchart

D7 receiving 3-bit T's
M[AR] > IR > AR
M[AR] > AR

SC < 0

MEMORY REFERENCE INSTRUCTIONS FLOWCHART
7 instructions, all have to do with fetching the memory
7 clock cycles

***reset the sequence counter “___<- 0”

PC fetches an instruction then it gets incremented
100 → 101
BSA__________L2 (Instr Reg)
return address (address continues)
resume the instruction from the original caller

L2: has the location to save 101
in the memory of AR

BSA
program counter is saved in the memory location of AR
then you increment AR by 1

every time PC receives instruction, increment it

REGISTER REFERENCE INSTRUCTIONS

CL clear
CM compliment (reverse the bits)

3 categories of instructions for modern computer
memory reference, register reference, I/O

I/O AND INTERRUPT
handshaking, etc